Signature

Signature wall mounted basin mixer With drainage

FFAS1704-1015L0BC0

FEATURES

- Low lead brass, strong and durable

- High quality ceramic valve for longer usage

- Ceramic cartridge tested = 500,000 times

- Neoperl aerator 1.5 GPM

- With  Brass Press Action Pop-up Drain

- With normal packaging

- Flow rate @ 0.1MPa: 3.8 L/min for spout

SPECIFICATIONS

In Wall Basin mixer faucet

One lever handle

Spout reach:  198 mm

FINISHES AVAILABILITY

Chrome (- CP)

AWARDS WON

N/A

SHIPPING WEIGHT

Product gross weight:  3.256kg /set

Product net weight:      3.056kg /set

STANDARDS CRITERIA

GB 18145-2014

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice, we assume no liability for the use of obsolete dimensions.

# Text boxes

DIMENSIONAL DRAWING