Compact Codie (Thailand)

vdalve & flexible hose CCAS2074-2200400C0

S-TRAP

P-TRAP

This document is the property of American Standard. It can neither be reproduced, nor communicated, without authorization.

American Standard reserves the right to change dimensions and specifications without notice; we assume no liability for the use of obsolete dimensions.

# Text boxes

SPECIFICATIONS

- Flushing Platform: Wash Down

- Flushing Type: Dual flush / Top push

- Litres Per Flush: 3/4.2 lpf

- S/P-Trap: S trap & P trap

- Roughing in: 305mm floor discharge/190mm wall discharge

- Bowl Shape: Semi-elongated

- Overall Dimensions (LxWxH):

L680xW386xH782mm

- Height to Rim: 390mm

- Material: Vitreous China

- Color: White only (6D)

FEATURES

- Contemporary design

- Full skirted

- Comfort Seat and Slow Close

- ComfortClean Glaze

- Water Saving: 3/4.2L Dual flush

Close Coupled Toilet

CL24075-6DAxxxx

INCLUDED COMPONENTS

- Slow closing seat

- Dual tank fitting set

- Connector

- Floor fixing set

- Stop valve (optional)

- Installation manual

SHIPPING WEIGHT AND DIMENSIONS

- Gross Weight: 53.40 kg

- Net Weight: 42.61 kg

STANDARDS CRITERIA

- TIS-792:2011

- PNS 156:2010

- MS 1522:2011

- SS 378-1996

- ASME-A112.19.2-2013

- SNI 03-0797-2006

DIMENSIONAL DRAWING